2011

# District Championships

# Written Technical Information Test

HVAC-R Technology

2011 District HVAC-R Technology

Directions:  Please do not write on this test.  Put your answers on the sheet provided.

| 1. | A blower motor is rated for 5 Amps at 220 volts. If the same horsepower motor is wired for 100 volts, the amp draw will be __________. a) 10 Amps b) 2.5 Amps c) 8 Amps d) 20 Amps |
| --- | --- |
| 2. | OHM's low is stated at I = E/R. I stands for __________. a) Volts b) OHM c) Watts d) Amps |
| 3. | A 3 phase motor has an ohm reading from L1-L2 of 6 ohms. L1-L3 would be _______ ohms when the motor is 220 volts. a) 12 b) 0 c) 9 d) 6 |
| 4. | A high pressure control is setup to cut out at 380 lbs, cut in at 300 lbs. The differential would be _______________. a) -80 lbs b) 80 lbs c) 680 lbs d) 80 |
| 5. | Ten degrees is a good temperature difference across a water cooled condenser. Water entering at 55 should leave at ___________. a) 45 b) 65 c) 55 d) None of the above |
| 6. | A single phase motor windings have been checked for ohm ratings. R-S is 15 OHMS, R-C is 3 OHM, S-C would be _____________. a) 18 b) 45 c) 5 d) 12 |
| 7. | Transfer of heat occurs from a warmer object to a ________________. a) Warmer object b) Object of the same temperature c) Cooler object d) A liquid of the same temperature |
| 8. | At sea level, water will boil at _______ Fahrenheit. a) 32 b) 100 c) 273 d) None of the above |
| 9. | When converting Fahrenheit degrees to Celsius degrees, the correct formula is __________. a) C = 9/5 (F + 32) b) C = 5/9 (F - 32) c) F = (9/5 x C) + 32 d) F = (5/9 x C) - 32 |
| 10. | 48,000 BTU (British Thermal Units) is _________ TONS. a) 4 b) 3 c) 2 d) 5 |
| 11. | An opening for a standard size grill is generally 2 times the duct size. A duct size of 12 x 8 would require a return air grill to be _____________. a) 24 x 16 b) 12 x 16 c) 20 x 12 d) 24 x 24 |
| 12. | Water freezes at 32O Fahrenheit and _________ centigrade Kelvin. a) 0 b) 100 c) -273 d) 273 |
| 13. | R-12 is identified by the name ______________. a) Monochlorodifluoromethane b) Dichlorodifluromethane c) Trichloromonofluoromethane d) Monchlorodifluoromethane |
| 14. | Air conditioning systems require _______ cfm per ton to operate properly. a) 600 b) 800 c) 400 d) 200 |
| 15. | To remove the refrigerant from a system without any testing or processing and to be put back into the same system is called _______________. a) Recovery b) Renew c) Reclaim d) Recycle |
| 16. | The refrigerant number means __________________. a) The refrigerants chemical makeup b) The ozone depletion number c) The temperature application d) The oil computability |
| 17. | Which of the following refrigerants is a CFC type refrigerant? a) R-22 b) R-123 c) R-134a d) R-12 |
| 18. | The condenser __________________. a) Rejects the heat from the refrigerant b) Controls the refrigerant flow throughout the system c) Ads superheat to the refrigerant d) All of the above |
| 19. | The evaporator in a refrigeration system _________________. a) Reduces the boiling point of the refrigerant b) Condenses the refrigerant c)Absorbs heat from the product to be cooled d) Compresses the refrigerant vapor |
| 20. | The refrigerant leaving the compressor is ________________. a) A super-heated vapor b) Sub-cooled liquid c) Super-heated liquid d) None of the above |
| 21. | The refrigerant in a refrigeration system changes state in the __________________. a) Condenser and Compressor b) Compressor and Expansion device c) Expansion device and Evaporator d) Condenser and Evaporator |
| 22. | Moisture in a liquid state must be _______ before it can be removed with a vacuum pump. a) Vaporized b) Condensed c) Cooled d) Solidified |
| 23. | Which of the following represents the lowest vacuum? a) 10 psia b) 5" Hg VAC c) 5 psig d) 1000 Microns |
| 24. | The color of a refrigerant cylinder indicates __________________. a) The type of refrigerant inside b) The Hazmat rating c) It is a recovery cylinder d) A and b |
| 25. | While the compressor is running, the discharge valve should never be _______________. a) Front-seated b) Back-seated c) Used or adjusted d) Mid-seated |
| 26. | When a refrigeration system pump downs, where is the refrigerant stored? a) Receiver b) Evaporator c) Condenser d) Both A and C |
| 27. | The solenoid valve on a pump down system __________________. a) Controls liquid refrigerant flow b) Changes system capacity c) Bypasses hot gas d) Controls suction pressure at the compressor inlet |
| 28. | When the load on the evaporator increases, the TX valve _____________. a) Increases the flow of refrigerant b) Decreases the flow of refrigerant c) Maintains constant head pressure d) Decreases the pressure drop across the evaporator |
| 29. | The TXV sensing bulb is mounted ______________. a) On the liquid line between the condenser and the TX valve b) At the inlet to the condenser c) On the suction line on the evaporator outlet d) On the compressor discharge line |
| 30. | What could happen if a semi-hermetic compressor is operated with the suction service valve back-seated and the discharge valve front-seated? a) The system will pump down b) The system will pump out c) The head of the compressor may blow off d) The compressor capacity will increase |
| 31. | The refrigerant in a condenser in a refrigeration system __________________. a) Absorbs heat b) Gives up heat c) Changes to a vapor d) Is under lower pressure than the evaporator |
| 32. | Which of the following condensers is the most efficient? a) Forced draft air cooled b) Induced draft air cooled c) Water-cooled parallel flow d) Water-cooled counter flow |
| 33. | The refrigerant leaving the compressor is referred to as _____________. a) Hot liquid refrigerant b) Hot gas c) A partial liquid d) Condensed vapor |
| 34. | During the defrost cycle of a forced draft low temperature evaporator, the evaporator fan would ___________. a) remain on to speed up the defrost b) turn off c) cycle with the condenser d) cycle with the compressor |
| 35. | A forced draft medium temperature evaporator would _____________. a) be defrosted by off-cycle defrost b) not need to be defrosted c) need electric defrost d) need a hot gas defrost |
| 36. | C.F.C’s can no longer be manufactured after _________. a) November 25, 1991 b) January 1, 1999 c) January 1, 1996 d) September 15, 1995 |
| 37. | The Clean Air Act of 1990 states ____________________. a) A technician must be licensed to work with refrigerants b) Must document all equipment repairs c) A technician can no longer vent refrigerants into the atmosphere d) None of the above |
| 38. | A technician with a Universal License is qualified to work on which type of system? a) High pressure system containing 20lbs of R-22 b) A dehumidifier c) Low pressure system containing 250lbs of R-134A d) All of the above |
| 39. | A technician is responsible to recover 80% if the system change when __________. a) The compressor is running b) The compressor is in operative c) A passive method is used d) None of the above |
| 40. | The ozone layer protects the earth from _____________. a) Hydro carbons b) Damaging ultra violet rays c) Global warming d) Warming of the earths poles |
| 41. | Low pressure refrigerants are _____ category. a) Type 1 b) Type 2 c) Type 3 d) None of the above |
| 42. | Technicians working on equipment with more than 50lbs refrigerant under high pressure must have a _____________. a) Type 1 License b) Type 2 License c0 Universal License d) Both B and C |
| 43. | Technicians working on a system with less than 5lbs refrigerant must have a _________. a) Type 1 Recovery License b) Type 2 Recovery License c) Type 3 Recovery License d) All of the above |
| 44. | Which chemical is most dangerous to the earth’s atmosphere? a) Carbon b) Oxygen c) Flourine d) Chlorine |
| 45. | All recovery equipment manufactured after November 15, 1993 must _____________. a) Be equipped with low loss fittings b) Be able to handle more than one refrigerant c) Be properly marked d) Be certified by an E.P.A. approval testing group |
| 46. | Refrigerant R-134A is a _____ refrigerant. a) H.F.C. b) C.F.C. c) H.C.F.C. d) None of the above |
| 47. | The penalty for venting refrigerants to the atmosphere is ________. a) $2,500.00 b) $10,000.00 c) $25,000.00 d) $100,000.00 |
| 48. | A refrigerant cylinder should or vessel should contain up to ______% of the maximum capacity. a) 90 b) 100 c) 70 d) 80 |
| 49. | Which refrigerants have the greatest effect on the ozone? a) C.F.C. b) H.C.F.C. c) H.F.C. d) All of the above |
| 50. | A.R.I. Standards must be met when _________ of refrigerants. a) Recycling b) Reclaiming c) Recovery d) Disposing |
| 51. | What is the name of the process in which we can heat a piece of hard drawn copper tubing and let it cool to make it soft? a) Superheating b) Un-solidifying c) Annealing d) None of the above |
| 52. | How many feet of ACR soft copper tubing comes in a standard roll? a) 50 b) 75 c) 20 d) 25 |
| 53. | When joining PVC tubing with cement, the tubing must be cut to length, chamfered and ________ before gluing. a) Sanded b) Cleaned with a primer c) Crimped d) Threaded |
| 54. | In order to thread steel pipe, _______ should be used to prevent damage to the pipe and cutting dies. a) Mineral oil b) Cutting oil c) Motor oil d) Fuel oil |
| 55. | The abbreviation for the plastic pipe used in hot and cold water distribution systems. a) PVC b) ABS c) CPVC d) CPV |
| 56. | The type of plastic material used for water and gas supply lines. a) Polyethylene b) Polybutylene c) CPVC d) CCST |
| 57. | The abbreviation for the plastic pipe used in systems for waste drains and low temperature vents on a high efficiency gas furnace. a) ABS b) CPVC c) PVC d) A and B |
| 58. | The abbreviation for the plastic pipe used in systems for waste drains and low temperature vents on a high efficiency gas furnace. a) ABS b) CPVC c) PVC d) A and B |
| 59. | Type of material which shall not be used in piping natural gas. a) Black steel b) Corrugated stainless steel c) Black cast iron d) Black malleable iron |
| 60. | _______ type copper tubing shall be used in the field piping of a refrigeration system. a) L b) M c) K d) ACR |
| 61. | The use of ________based flux should be used when soft soldering copper materials together. a) Petroleum b) Water c) Oil d) Iron |
| 62.. | When tubing is cut with a tubing cutter, a burr is produced in the process. What step in the pipe preparation process must be taken to remove this burr? a) Tubing must be sanded b) Tube end must be heated c) Tube end must have flux applied to it d) Tube end must be reamed |
| 63. | Molten solder flows between the two base metals being soldered because ___________. a) The atmospheric pressure pushes it in b) Of capillary action c) There are no surface pores in the base metal d) The tubing surface melts and the pressure differential forces it in |
| 64. | The proper type of flame from an oxy-acetylene torch for silver brazing is _________. a) Long tail flame b) Neutral flame c) Oxidizing flame d) Carbonizing flame |
| 65. | When soldering or brazing, the filler material is __________. a) Heated directly by the flame of the heat source b) Heated by the surrounding air c) Used to oxidize the metal d) Melted by heat from the tubing and fitting |
| 66. | Brazing is done at __________ soldering. a) the same temperature as b) lower temperatures than c) higher temperatures than d) temperatures that can be higher or lower than |
| 67. | Liquid entering the suction line will cause ____________. a) over heating of the compressor b) starving of the evaporator c) frost on the suction line. d) None of the above. |
| 68. | Which type of compressor uses veins to compress the refrigerant? a) scroll b) screw c) rotary d) reciprocating |
| 69. | The red hose on the manifold gets hooked up to the _____________. High side b) Low side c) Receiver d) Condenser |
| 70. | An evaporator fan control keeps _____________. a) Fan off after defrost b) Fan running at the right speed c) Fan running all the time d) Fan on only in defrost mode |
| 71. | Rooftop units should be installed ____________. a) Lower than the rooftop level b) At least 2” above roof line c) At least 12” above roof line d) 2 feet above roof line |
| 72. | When bending cooper tubing a _____ should be used. a) Conduit bender b) Flaring block c) Hammer d) Spring bender |
| 73. | A system undercharge can be detected by _________________. a) Frosted suction line b) Too much cooling c) Frosted metering device d) Low super heat |
| 74. | Temperatures inside the cabinet that are too cold may be caused by ____________. a) Faulty thermostat b) Defective relay c) Bad fan motor d) Stuck compressor |
| 75. | When moving a nitrogen cylinder, the cap should be a) Readily available b) Put on very loosely c) Tightly secured d) Color coded to match the tank |
| 76. | The ____________ sets the pace for SkillsUSA. a) Motto b) Program of Work c) Creed d) Pledge |
| 77. | What is the most important element of the SkillsUSA organization? a) The individual b) The officers c) The board of directors d) The advisor |
| 78. | SkillsUSA has how many “I believes” in it? a) 5 b) 9 c) 6 d) 7 |
| 79. | The ________________ represent the individual. a) Hands b) Torch c) Shield d) Orbital circles |
| 80. | The ______________ represents the industrial society. a) Orbital circles b) Hands c) Gear d) Shield |
| 81. | The first of __________ starts a new year for the SkillsUSA Organization. a) January b) March c) July d) September |
| 82. | What is the highest degree that a person can receive in SkillsUSA? a) The Master Degree b) The American Degree c) The International Degree d) The Professional Degree |
| 83. | When did the organization’s name change from SkillsUSA-VICA to SkillsUSA? a) July 4, 1999 b) September 1, 2004 c) January 1, 2000 d) June 1, 2000 |
| 84. | “Preparing for Leadership in the World of Work” is: The SkillsUSA Theme b) The SkillsUSA Motto c) The SkillsUSA Creed d) The SkillsUSA Purpose |
| 85. | “I Believe in the American Way of Life” is a part of: SkillsUSA Motto b) SkillsUSA Theme c) SkillsUSA Pledge d) SkillsUSA Creed |
| 86. | Minutes are a record of: a) What was said b) The opinion of the secretary c) Business transacted d) All of the above |
| 87. | How many main motions may be on the floor at any one time? a) 1 b) 2 c) 3 d) 4 |
| 88. | Three taps of the gavel means a) Sit down b) Stand up c) Meeting adjourned d) Motion passed |
| 89. | When a motion is made in a meeting, you a) Should begin to discuss it b) Should get up and leave if you don’t like it c) Must vote on it immediately d) Need a second to discuss it |
| 90. | A listing of “Personalized” Meeting events written in a logical sequence is called a/an: a) Agenda b) Order of Business c) Committee Report Form d) Program of Work |
| 91. | Training in the opening and closing ceremonies develops: a) Poise b) Teamwork c) Voice Control d) Both A & B |
| 92. | When representing SkillsUSA, your ____________ gives an important first impression. a) Skill b) Manners c) Voice d) Appearance |
| 93. | What is the accepted gratuity for good service in a restaurant? a) 5-10% b) 15-20% c) 25-50% d) 50-60% |
| 94. | ___________________setting is an important factor in being successful. a) Time b) Goal c) Assignment d) Home |
| 95. | When assembling your portfolio for employment in your profession, which of the following should not be included in your portfolio: a) Résumé b) Letters of recommendation c) Job application d) Samples of your best work |
| 96. | What is the written statement from a person in authority who acts as an endorsement of your positive attributes? a) Application b) Résumé c) Letter of recommendation d) Portfolio |
| 97. | What is the term given to an unpaid experience in which you observe and participate in a specific occupation? a) Coop b) Internship c) Apprenticeship d) Job Shadowing |
| 98. | Which term describes a person’s income before any deductions? a) Interest b) Gross c) Net d) Viability |
| 99. | A method of creating a lot of ideas in a short period of time and expanding your thinking is called? Teaming b) reading c) developing d) brainstorming |
| 100. | According to the Leadership Handbook, a public speech should be broken down into what three basic parts? a) Instruction, speech and summary b) Opening, examples and review c) Introduction, body and closing d) Review, evidence and thank you |